## Slide 1: CS2100 Tutorial 11
Cache
While waiting, do fill the end-of-sem feedback
https://blue.nus.edu.sg
Slides by Theodore, adapted from Prof. Aaron’s slides

## Slide 2: Errata / Additional info for pipelining
! For exams ! (Checked with Prof. Anandha on Wed)
For non-ideal pipeline with branching:
  Resolution stages: MEM (default), ID (early)
  Branch prediction: no prediction, predict not taken (default), predict taken
  Reordering of instructions: no reordering unless otherwise mentioned
You have the option to ask in exam if you think an assumption is not stated clearly

## Slide 3: Recap
Types of cahces
  direct mapped cache
  n-way associative
  fully associative

## Slide 4: Q1a
Info from question:
  Machine is byte-addressable
  Word size is 16 bits (2 bytes)
  Address space spanned by 32 bits
  Cache:
    16 blocks
    2 word in a block

## Slide 5: Q1a
Info from question:
  Machine is byte-addressable
  Word size is 16 bits (2 bytes)
  Address space spanned by 32 bits
  Cache:
    16 blocks
    2 words in a block
Valid words:
0x00
0x02
0x04
…
Invalid words (but valid address):
0x01
0x03
0x05
…
16 blocks: index of size 4

## Slide 6: Q1a
Info from question:
  Machine is byte-addressable
  Word size is 2 bytes  last bit needs to be 0 for a valid word
  Address space spanned by 32 bits
  Cache:
    16 blocks  index size 4
    2 words in a block
Example address: 0b0000 0000 0000 0000 0000 0000 0000 0000

## Slide 7: Q1a
Info from question:
  Machine is byte-addressable
  Word size is 2 bytes  last bit needs to be 0 for a valid word
  Address space spanned by 32 bits
  Cache:
    16 blocks  index size 4
    2 words in a block
Example address: 0b0000 0000 0000 0000 0000 0000 0000 0000

## Slide 8: Q1a

## Slide 9: Q1a

## Slide 10: Q1b

## Slide 11: Q1a

## Slide 12: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
MIPS
Addresses are 32 btis
Words are 4 bytes each
 consecutive words differ by 4 in their address
 all words' addresses end with 00
4 blocks in cache, 2 words each
 1 bit to distinguish the different words
 2 bits for index
0b0000 0000 0000 0000 0000 0000 0000 0000

## Slide 13: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
$t0 starts at 1; $t2 = $t0 x 4
$t3 = $s0 + $t2
 first lw is on memory 0x1000 + 4 = 0x1004
$t4 = $s1 + $t2
 second lw is on memory 0x4010 + 4 = 0x4014
And first sw is on $t3 – 4
 0x1004 – 4 = 0x1000
At the end of iteration, $t0++.
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 

## Slide 14: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[1000] | M[1004]
1 |  |  | 
2 | 0x0…0200 | M[4010] | M[4014]
3 |  |  | 
$t0 starts at 1; $t2 = $t0 x 4
$t3 = $s0 + $t2
 first lw is on memory 0x1000 + 4 = 0x1004
$t4 = $s1 + $t2
 second lw is on memory 0x4010 + 4 = 0x4014
And first sw is on $t3 – 4
 0x1004 – 4 = 0x1000
At the end of iteration, $t0++.

## Slide 15: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[1000] | M[1004]
1 |  |  | 
2 | 0x0…0200 | M[4010] | M[4014]
3 |  |  | 
$t0 starts at 1; $t2 = $t0 x 4
$t3 = $s0 + $t2
 first lw is on memory 0x1000 + 4 = 0x1004
$t4 = $s1 + $t2
 second lw is on memory 0x4010 + 4 = 0x4014
And first sw is on $t3 – 4
 0x1004 – 4 = 0x1000
At the end of iteration, $t0++.

## Slide 16: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[1000] | M[1004]
1 |  |  | 
2 | 0x0…0200 | M[4010] | M[4014]
3 |  |  | 
$t0 starts at 1; $t2 = $t0 x 4
$t3 = $s0 + $t2
 first lw is on memory 0x1000 + 4 = 0x1004
$t4 = $s1 + $t2
 second lw is on memory 0x4010 + 4 = 0x4014
And first sw is on $t3 – 4
 0x1004 – 4 = 0x1000
At the end of iteration, $t0++.

## Slide 17: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) On the first iteration,
lw cold miss (1004); lw cold miss (4014); sw hit (1000)
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[0x1000] | M[0x1004]
1 |  |  | 
2 | 0x0…0200 | M[0x4010] | M[0x4014]
3 |  |  | 

## Slide 18: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) On the first iteration,
lw cold miss (1004); lw cold miss (4014); sw hit (1000)
On the second iteration,
lw cold miss (1008); lw cold miss (4018); sw hit (1004)
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[0x1000] | M[0x1004]
1 | 0x0…0080 | M[0x1008] | M[0x100C]
2 | 0x0…0200 | M[0x4010] | M[0x4014]
3 | 0x0…0200 | M[0x4018] | M[0x401C]

## Slide 19: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) On the first iteration,
lw cold miss (1004); lw cold miss (4014); sw hit (1000)
On the second iteration,
lw cold miss (1008); lw cold miss (4018); sw hit (1004)
At this point, cache is warmed up!
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[0x1000] | M[0x1004]
1 | 0x0…0080 | M[0x1008] | M[0x100C]
2 | 0x0…0200 | M[0x4010] | M[0x4014]
3 | 0x0…0200 | M[0x4018] | M[0x401C]

## Slide 20: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) First two iterations: 4 misses, 2 hits
At this point, cache is warmed up!
On the third iteration,
lw hit (100C), lw hit (401C), sw hit (1008)
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[0x1000] | M[0x1004]
1 | 0x0…0080 | M[0x1008] | M[0x100C]
2 | 0x0…0200 | M[0x4010] | M[0x4014]
3 | 0x0…0200 | M[0x4018] | M[0x401C]

## Slide 21: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) First two iterations: 4 misses, 2 hits
At this point, cache is warmed up!
On the third iteration,
lw hit (100C), lw hit (401C), sw hit (1008)
On the fourth iteration,
lw miss (1010), lw miss (4020), sw hit (100C)
Index | Tag | Word 0 | Word 1
0 | 0x0…0080 | M[0x1000] | M[0x1004]
1 | 0x0…0080 | M[0x1008] | M[0x100C]
2 | 0x0…0200 | M[0x4010] | M[0x4014]
3 | 0x0…0200 | M[0x4018] | M[0x401C]

## Slide 22: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) First two iterations: 4 misses, 2 hits
At this point, cache is warmed up!
On the third iteration,
lw hit (100C), lw hit (401C), sw hit (1008)
On the fourth iteration,
lw miss (1010), lw miss (4020), sw hit (100C)
Index | Tag | Word 0 | Word 1
0 | 0x0…0200 | M[0x4020] | M[0x4024]
1 | 0x0…0080 | M[0x1008] | M[0x100C]
2 | 0x0…0080 | M[0x1010] | M[0x1014]
3 | 0x0…0200 | M[0x4018] | M[0x401C]

## Slide 23: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) First two iterations: 4 misses, 2 hits
At this point, cache is warmed up!
On the third iteration,
lw hit (100C), lw hit (401C), sw hit (1008)
On the fourth iteration,
lw miss (1010), lw miss (4020), sw hit (100C)
On the fifth iteration,
lw hit (1014), lw hit (4024), sw hit (1010)
Index | Tag | Word 0 | Word 1
0 | 0x0…0200 | M[0x4020] | M[0x4024]
1 | 0x0…0080 | M[0x1008] | M[0x100C]
2 | 0x0…0080 | M[0x1010] | M[0x1014]
3 | 0x0…0200 | M[0x4018] | M[0x401C]

## Slide 24: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) First two iterations: 4 misses, 2 hits
At this point, cache is warmed up!
On the third iteration,
lw hit (100C), lw hit (401C), sw hit (1008)
On the fourth iteration,
lw miss (1010), lw miss (4020), sw hit (100C)
On the fifth iteration,
lw hit (1014), lw hit (4024), sw hit (1010)
On the sixth iteration,
lw miss (101C), lw miss (4028), sw hit (1014)

## Slide 25: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) First two iterations: 4 misses, 2 hits
At this point, cache is warmed up!
On the third iteration,
lw hit (100C), lw hit (401C), sw hit (1008)
On the fourth iteration,
lw miss (1010), lw miss (4020), sw hit (100C)
On the fifth iteration,
lw hit (1014), lw hit (4024), sw hit (1010)
On the sixth iteration,
lw miss (101C), lw miss (4028), sw hit (1014)
repeats!

## Slide 26: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(c) First two iterations: 4 misses, 2 hits
At this point, cache is warmed up!
On the third iteration,
lw hit (100C), lw hit (401C), sw hit (1008)
On the fourth iteration,
lw miss (1010), lw miss (4020), sw hit (100C)
For every two iterations between 3 to 998 (498 times), there will be 4 hits and 2 misses
Iteration 999: lw hit, lw hit, sw hit (3 hits, 0 misses)
Total hits: 2 + 4*498 + 3 = 1997
Total miss: 4 + 2*498 + 0 = 1000
Miss rate: 1000/2997 = 33.37%
repeats!

## Slide 27: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(b) We can either go forwards (continue doing part a) or backwards (see what values are last cached)
Working backwards,
In iteration 999, we have lw from 0x1000 + 4*999 = 0x1F9C
lw from 0x4010 + 4*999 = 0x4FAC
sw to 0x1000 + 4*998 = 0x1F98
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 

## Slide 28: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(b) We can either go forwards (continue doing part a) or backwards (see what values are last cached)
Working backwards,
In iteration 999, we have lw from 0x1000 + 4*999 = 0x1F9C
lw from 0x4010 + 4*999 = 0x4FAC
sw to 0x1000 + 4*998 = 0x1F98
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 | 0x27D | M[0x4FA8] | M[0x4FAC]
2 |  |  | 
3 | 0xFC | M[0x1F98] | M[0x1F9C]

## Slide 29: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(b) We can either go forwards (continue doing part a) or backwards (see what values are last cached)
Working backwards,
In iteration 998, we have lw from 0x1000 + 4*998 = 0x1F98
lw from 0x4010 + 4*998 = 0x4FA8
sw to 0x1000 + 4*997 = 0x1F94
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 | 0x27D | M[0x4FA8] | M[0x4FAC]
2 | 0xFC | M[0x1F90] | M[0x1F94]
3 | 0xFC | M[0x1F98] | M[0x1F9C]

## Slide 30: Q2
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
(b) We can either go forwards (continue doing part a) or backwards (see what values are last cached)
Working backwards,
In iteration 997, we have lw from 0x1000 + 4*997 = 0x1F94
lw from 0x4010 + 4*997 = 0x4FA4
sw to 0x1000 + 4*996 = 0x1F90
Index | Tag | Word 1 | Word 2
0 | 0x27D | M[0x4FA0] | M[0x4FA4]
1 | 0x27D | M[0x4FA8] | M[0x4FAC]
2 | 0xFC | M[0x1F90] | M[0x1F94]
3 | 0xFC | M[0x1F98] | M[0x1F9C]

## Slide 31: Q3
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
MIPS
Addresses are 32 btis
Words are 4 bytes each
 consecutive words differ by 4 in their address
 all words' addresses end with 00
4 blocks in cache, 2 words each
 1 bit to distinguish the different words
 2 bits for index
0b0000 0000 0000 0000 0000 0000 0000 0000

## Slide 32: Q3b
start:
la $s0, A #PC=0x100
la $s1, B #PC=0x104
li $t0, 1 #PC=0x108
loop:
slt $t1, $t0, 1000 #PC=0x10c
beq $t1, $zero, endl #PC=0x110
sll $t2, $t0, 2 #PC=0x114
add $t3, $s0, $t2 #PC=0x118
lw $a0, 0($t3) #PC=0x11c
add $t4, $s1, $t2 #PC=0x120
lw $a1, 0($t4) #PC=0x124
add $v0, $a0, $a1 #PC=0x128
sw $v0, -4($t3) #PC=0x12c
addi $t0, $t0, 1 #PC=0x130
j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
See the code first before you start!
Instructions at 0x100-0x108 only executed once
Loop is at 0x10C to 0x134, no other branching other than j loop (and exit at 0x110)
Iterates 999 times fully,
On 1000th iteration just do 0x10C and 0x110

## Slide 33: Q3b
Index | Tag | Word 1 | Word 2
0 |  |  | 
1 |  |  | 
2 |  |  | 
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:

## Slide 34: Q3b
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 |  |  | 
2 |  |  | 
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:

## Slide 35: Q3b
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 |  |  | 
2 |  |  | 
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:

## Slide 36: Q3b
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 |  |  | 
2 |  |  | 
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 0, tag 0x8) – cold miss
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:

## Slide 37: Q3b
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 | 0x8 | 0x108 | 0x10C
2 |  |  | 
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:

## Slide 38: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 | 0x8 | 0x108 | 0x10C
2 |  |  | 
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit

## Slide 39: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 | 0x8 | 0x108 | 0x10C
2 |  |  | 
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)

## Slide 40: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 |  |  | 
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)

## Slide 41: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)

## Slide 42: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x8 | 0x100 | 0x104
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)
Instruction 9 conflict miss,
instruction 10 hit (index 0)

## Slide 43: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)
Instruction 9 conflict miss,
instruction 10 hit (index 0)
underlined: have been replaced

## Slide 44: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)
Instruction 9 conflict miss, inst 10 hit (index 0)
Instruction 11 conflict miss, inst 12 hit (index 1)
underlined: have been replaced

## Slide 45: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)
Instruction 9 conflict miss, inst 10 hit (index 0)
Instruction 11 conflict miss, inst 12 hit (index 1)
underlined: have been replaced

## Slide 46: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)
Instruction 9 conflict miss, inst 10 hit (index 0)
Instruction 11 conflict miss, inst 12 hit (index 1)
Instruction 13 conflict miss, inst 14 hit (index 2)
underlined: have been replaced

## Slide 47: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop) Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)
Instruction 9 conflict miss, inst 10 hit (index 0)
Instruction 11 conflict miss, inst 12 hit (index 1)
Instruction 13 conflict miss, inst 14 hit (index 2)
underlined: have been replaced

## Slide 48: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
Instruction 1: 0x100 (Index 0, tag 0x8) – cold miss
Instruction 2: 0x104 (Index 0, tag 0x8) – hit
Instruction 3: 0x108 (Index 1, tag 0x8) – cold miss
(Start of loop)
Iteration 1: 5 miss, 6 hit Instruction 4: 0x10C (Index 1, tag 0x8) – hit
Instruction 5 miss, instruction 6 hit (both index 2)
Instruction 7 miss, instruction 8 hit (both index 3)
Instruction 9 conflict miss, inst 10 hit (index 0)
Instruction 11 conflict miss, inst 12 hit (index 1)
Instruction 13 conflict miss, inst 14 hit (index 2)
underlined: have been replaced

## Slide 49: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (idx 2 changed)

## Slide 50: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (idx 2 changed)

## Slide 51: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x128 | 0x12C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (index 2 was also rewritten last loop)

## Slide 52: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x128 | 0x12C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (idx 2 changed)
Instructions 7 and 8 hit (index 3 from prev iteration)
Instruction 9 and 10 hit (index 0 from prev iteration)

## Slide 53: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x128 | 0x12C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (idx 2 changed)
Instructions 7 and 8 hit (index 3 from prev iteration)
Instruction 9 and 10 hit (index 0 from prev iteration)
Instruction 11 conflict miss, inst 12 hit (index 1)
Instruction 13 conflict miss, inst 14 hit (index 2)

## Slide 54: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (idx 2 changed)
Instructions 7 and 8 hit (index 3 from prev iteration)
Instruction 9 and 10 hit (index 0 from prev iteration)
Instruction 11 conflict miss, inst 12 hit (index 1)
Instruction 13 conflict miss, inst 14 hit (index 2)

## Slide 55: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (idx 2 changed)
Instructions 7 and 8 hit (index 3 from prev iteration)
Instruction 9 and 10 hit (index 0 from prev iteration)
Instruction 11 conflict miss, inst 12 hit (index 1)
Instruction 13 conflict miss, inst 14 hit (index 2)
Notice that the cache is identical to the end of iter 1

## Slide 56: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: 4 miss, 7 hit Instruction 4 miss, since index 1 was rewritten
Instruction 5 miss, instruction 6 hit (idx 2 changed)
Instructions 7 and 8 hit (index 3 from prev iteration)
Instruction 9 and 10 hit (index 0 from prev iteration)
Instruction 11 conflict miss, inst 12 hit (index 1)
Instruction 13 conflict miss, inst 14 hit (index 2)
Notice that the cache is identical to the end of iter 1

## Slide 57: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: 4 miss, 7 hit Iterations 3 – 999: same as Iteration 2

## Slide 58: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x9 | 0x128 | 0x12C
2 | 0x9 | 0x130 | 0x134
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: 4 miss, 7 hit Iterations 3 – 999: same as Iteration 2
Iteration 1000:
Instruction 4 miss (idx 1), instruction 5 miss (idx 2)

## Slide 59: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: 4 miss, 7 hit Iterations 3 – 999: same as Iteration 2
Iteration 1000:
Instruction 4 miss (idx 1), instruction 5 miss (idx 2)

## Slide 60: Q3b
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
Setup: 2 misses, 1 hit
(Start of loop)
Iteration 1: 5 miss, 6 hit
Iteration 2: 4 miss, 7 hit Iterations 3 – 999: same as Iteration 2
Iteration 1000:
Instruction 4 miss (idx 1), instruction 5 miss (idx 2)
Total:
Misses: 2 + 5 + 4*998 + 2 = 4001
Hits: 1 + 6 + 7*998 = 6993

## Slide 61: Q3a
start:
1 la $s0, A #PC=0x100
2 la $s1, B #PC=0x104
3 li $t0, 1 #PC=0x108
loop:
4 slt $t1, $t0, 1000 #PC=0x10c
5 beq $t1, $zero, endl #PC=0x110
6 sll $t2, $t0, 2 #PC=0x114
7 add $t3, $s0, $t2 #PC=0x118
8 lw $a0, 0($t3) #PC=0x11c
9 add $t4, $s1, $t2 #PC=0x120
10 lw $a1, 0($t4) #PC=0x124
11 add $v0, $a0, $a1 #PC=0x128
12 sw $v0, -4($t3) #PC=0x12c
13 addi $t0, $t0, 1 #PC=0x130
14 j loop #PC=0x134
endl:
Index | Tag | Word 1 | Word 2
0 | 0x9 | 0x120 | 0x124
1 | 0x8 | 0x108 | 0x10C
2 | 0x8 | 0x110 | 0x114
3 | 0x8 | 0x118 | 0x11C
We traced everything till the end :)

## Slide 62: Q4

## Slide 63: Bonus: Beyond CS2100
MIPS
  Was and is used for some microprocessors
  Current: Loongson / LoongArch is MIPS-compatible
  Numerous other architectures besides MIPS! x86/x86-64, ARM/Arm-64, RISC V, …
  If you’re interested in more assembly stuff:
    CS4212 Compiler Design – you’ll make your own C to x86-lite compiler
    CS2106 and some CEG Courses
    A bunch of assembly games (check them out on Steam) (not sponsored or endorsed by me)

## Slide 64: Bonus: Beyond CS2100
Logic Circuit
  Not going to see this much if you’re taking CS
  If interested in this – look into CG / EE-coded courses; may be able to audit
Caching
  If you are going to take CS2106 (Operating Systems), you will see something really similar under the Paging topic
  Idea is the same -- put data somewhere fast if you access it multiple times
  More replacement policies beyond LRU

## Slide 65: End of Tutorial 11
Slides uploaded on github.com/theodoreleebrant/TA-2425S1
Email: theo@comp.nus.edu.sg
Anonymous feedback:
bit.ly/feedback-theodore
(or scan on the right)
All the best for exams!
(Also reminder for me to take attendance)