## Slide 1: CS2100 Tutorial 10
Pipelining
Slides by Theodore, adapted from Prof. Aaron’s slides

## Slide 2: Recap
Stages in pipelining
  IF: Instruction Fetch
  ID: Instruction Decode (+ reading register file)
  EX: Execute (+ calculate address)
  MEM: memory access
  WB: write back
Extra registers between stages
Forwarding and Hazard Detection

## Slide 3: Recap
Hazards
  Structural hazards: simultaneous use of hardware (IF<>MEM, ID<>WB)
    Solved by separating instruction & data memory (IF <> MEM)
    Solved by writing on the 1st half of the cycle, and reading on the 2nd half (ID <> WB)
  Data dependency
    Read-After-Write / true data dependency
      e.g. add $1, $2, $2 followed by add $3, $1, $1 – possible to read before writing back
      e.g. lw $2, 0($1) followed by add $3, $2, $2 – possible to read before load word finishes
  Control dependency
    Usually with branches

## Slide 4: Q1. Signals of pipelined instructions
Do some checks:
  Any data dependencies?
  Any control dependencies?
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L2

## Slide 5: Q1. Signals of pipelined instructions
Do some checks:
  Any data dependencies? No
  Any control dependencies? No
Continue with the pipeline diagram
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L2

## Slide 6: Q1. Signals of pipelined instructions
Do some checks:
  Any data dependencies? No
  Any control dependencies? No
Continue with the pipeline diagram
sub $1, $2, $3
lw $6, 4($7)
beq $4, $5, L2
 | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
sub $1, $2, $3 | IF | ID | EX | MEM | WB |  | 
lw $6, 4($7) |  | IF | ID | EX | MEM | WB | 
beq $4, $5, L2 |  |  | IF | ID | EX | MEM | WB

## Slide 7
 | sub $1, $2, $3 | lw $6, 4 ($7) | beq $4, $5, L2
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
PC= 0xFFC
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
sub $1, $2, $3
PC= 0xFF8
0x00430822

## Slide 8
 | sub $1, $2, $3 | lw $6, 4 ($7) | beq $4, $5, L2
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
RegWrite = 1
MemtoReg = 0
PC= 0x1000
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
PC= 0xFFC
0x8CE60004
sub $1, $2, $3
2
3
RegDst = 1
ALUOp = 2
ALUSrc = 0
Branch = 0
MemRead = 0
MemWrite = 0

## Slide 9
 | sub $1, $2, $3 | lw $6, 4 ($7) | beq $4, $5, L2
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
RegWrite = 1
MemtReg = 1
PC= 0x1004
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
PC= 0x1000
0x1085FC3F
beq $4, $5, L2
7
X
RegDst = 0
ALUOp = 0
ALUSrc = 1
Branch = 0
MemRead = 1
MemWrite = 0
RegWrite = 1
MemtoReg = 0
Branch = 0
MemRead = 0
MemWrite = 0
sub $1, $2, $3
0
1
2

## Slide 10
 | sub $1, $2, $3 | lw $6, 4 ($7) | beq $4, $5, L2
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
RegWrite = 0
MemtoReg = X
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
beq $4, $5, L2
4
5
RegDst = X
ALUOp = 2
ALUSrc = 0
Branch = 1
MemRead = 0
MemWrite = 0
RegWrite = 1
MemtoReg = 1
Branch = 0
MemRead = 1
MemWrite = 0
sub $1, $2, $3
1
0
0
RegWrite = 1
MemtoReg = 0
0
0
0

## Slide 11
 | sub $1, $2, $3 | lw $6, 4 ($7) | beq $4, $5, L2
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
beq $4, $5, L2
RegWrite = 0
MemtoReg = X
Branch = 1
MemRead = 0
MemWrite = 0
sub $1, $2, $3
1
0
0
RegWrite = 1
MemtoReg = 1
0
0
1
1
0
1

## Slide 12
 | sub $1, $2, $3 | lw $6, 4 ($7) | beq $4, $5, L2
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
lw $6, 4($7)
beq $4, $5, L2
RegWrite = 0
MemtoReg = X
1
0
0
1
1
6
0x100

## Slide 13
 | sub $1, $2, $3 | lw $6, 4 ($7) | beq $4, $5, L2
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
beq $4, $5, L2
0
X

## Slide 14: Q2. Tracing execution
Do some checks:
  Any data dependencies?
  Any control dependencies?
add $1, $2, $3
add $1, $1, $3
add $1, $1, $1

## Slide 15: Q2. Tracing execution
Do some checks:
  Any data dependencies? Yes
    Any forwarding? Yes
  Any control dependencies? No
add $1, $2, $3
add $1, $1, $3
add $1, $1, $1

## Slide 16: Q2. Tracing execution
Do some checks:
  Any data dependencies? Yes
    Any forwarding? Yes
  Any control dependencies? No
add $1, $2, $3
add $1, $1, $3
add $1, $1, $1
 | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
add $1, $2, $3 | IF | ID | EX | MEM | WB |  | 
add $1, $1, $3 |  | IF | ID | EX | MEM | WB | 
add $1, $1, $1 |  |  | IF | ID | EX | MEM | WB

## Slide 17: Q2. Tracing execution
Do some checks:
  Any data dependencies? Yes
    Any forwarding? Yes
  Any control dependencies? No
add $1, $2, $3
add $1, $1, $3
add $1, $1, $1
 | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7
add $1, $2, $3 | IF | ID | EX | MEM | WB |  | 
add $1, $1, $3 |  | IF | ID | EX | MEM | WB | 
add $1, $1, $1 |  |  | IF | ID | EX | MEM | WB
?
Note:
WB > EX forwarding happens, but loses in priority to MEM > EX fwd.

## Slide 18
 | add $1, $2, $3 | add $1, $1, $3 | add $1, $1, $1
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead
PC= 0x104
add $1, $2, $3
PC= 0x100
0x00430820

## Slide 19
 | add $1, $2, $3 | add $1, $1, $3 | add $1, $1, $1
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
PC= 0x108
add $1, $1, $3
PC= 0x104
0x00230820
add $1, $2, $3
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
3
1
2

## Slide 20
 | add $1, $2, $3 | add $1, $1, $3 | add $1, $1, $1
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
PC= 0x10c
add $1, $1, $3
PC= 0x108
0x00210820
add $1, $2, $3
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
3
1
1
add $1, $1, $1
1

## Slide 21
 | add $1, $2, $3 | add $1, $1, $3 | add $1, $1, $1
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
add $1, $1, $3
add $1, $2, $3
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
1
1
1
add $1, $1, $1
1
1
MEM->EX forwarding

## Slide 22
 | add $1, $2, $3 | add $1, $1, $3 | add $1, $1, $1
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
add $1, $1, $3
add $1, $2, $3
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
add $1, $1, $1
1
1
1
WB->EX forwarding
MEM->EX forwarding
MEM->EX forwarding wins

## Slide 23
 | add $1, $2, $3 | add $1, $1, $3 | add $1, $1, $1
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead

## Slide 24
 | add $1, $2, $3 | add $1, $1, $3 | add $1, $1, $1
Cycle 1 | IF |  | 
Cycle 2 | ID | IF | 
Cycle 3 | EX | ID | IF
Cycle 4 | MEM | EX | ID
Cycle 5 | WB | MEM | EX
Cycle 6 |  | WB | MEM
Cycle 7 |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead

## Slide 25: Q3. Tracing execution
Do some checks:
  Any data dependencies?
  Any control dependencies?
add $1, $2, $3
lw $1, 0($1)
add $1, $1, $1
add $3, $2, $1

## Slide 26: Q3. Tracing execution
Do some checks:
  Any data dependencies? Yes
  Any control dependencies? No
add $1, $2, $3
lw $1, 0($1)
add $1, $1, $1
add $3, $2, $1

## Slide 27: Q3. Tracing execution
Do some checks:
  Any data dependencies? Yes
  Any control dependencies? No
add $1, $2, $3
lw $1, 0($1)
add $1, $1, $1
add $3, $2, $1

## Slide 28: Q3. Tracing execution
Do some checks:
  Any data dependencies? Yes
  Any control dependencies? No
add $1, $2, $3
lw $1, 0($1)
add $1, $1, $1
add $3, $2, $1
 | Cycle 1 | Cycle 2 | Cycle 3 | Cycle 4 | Cycle 5 | Cycle 6 | Cycle 7 | Cycle 8 | Cycle 9
add $1, $2, $3 | IF | ID | EX | MEM | WB |  |  |  | 
lw $1, 0($1) |  | IF | ID | EX | MEM | WB |  |  | 
add $1, $1, $1 |  |  | IF | ID | (ID) | EX | MEM | WB | 
add $3, $2, $1 |  |  |  | IF | (IF) | ID | EX | MEM | WB

## Slide 29
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead
PC= 0x104
add $1, $2, $3
PC= 0x100
0x00430820

## Slide 30
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
PC= 0x108
add $1, $2, $3
PC= 0x104
0x8c210000
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
3
1
2
lw $1, 0($1)

## Slide 31
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
PC= 0x10c
PC= 0x108
0x00210820
add $1, $2, $3
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
1
X
1
add $1, $1, $1
1
lw $1, 0($1)

## Slide 32
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
PC = 0x110
PC= 0x10c
0x00411820
add $1, $2, $3
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
1
1
1
add $1, $1, $1
1
lw $1, 0($1)
add $3, $2, $1
1
HAZARD = 1

## Slide 33
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
PC = 0x110
PC= 0x10c
0x00411820
add $1, $2, $3
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
1
1
1
add $1, $1, $1
1
NOP!
add $3, $2, $1
1
lw $1, 0($1)
0

## Slide 34
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
1
3
2
add $1, $1, $1
NOP!
add $3, $2, $1
1
lw $1, 0($1)
1
1
WB-EX forwarding to both ALU operands
WB-EX forwarding to both ALU operands

## Slide 35
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
ID/EX.MemRead
ID/EX.RegisterRt
IF/ID.RegisterRt
IF/ID.RegisterRd
IF/ID.RegisterRt
IF/ID.RegisterRs
add $1, $1, $1
NOP!
add $3, $2, $1
1
1

## Slide 36
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead

## Slide 37
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead

## Slide 38
 | add $1, $2, $3 | lw $1, 0 ($1) | add $1, $1, $1 | add $3, $2, $1
1 | IF |  |  | 
2 | ID | IF |  | 
3 | EX | ID | IF | 
4 | MEM | EX | ID | IF
5 | WB | MEM |  | 
6 |  | WB | EX | ID
7 |  |  | MEM | EX
8 |  |  | WB | MEM
9 |  |  |  | WB
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead

## Slide 39
Q4a
Reg
# PC = 0x10c
add $3,$2,$1
# PC = 0x108
beq $1, $0, L
# PC = 0x104
lw $1, 0($1)
# PC = 0x100
add $1, $2, $3
ALU
IF
Reg
Mem
Reg
ALU
IF
Reg
Mem
Reg
IF
ALU
Mem
Reg
bubble
Not taken
If not taken
# PC = 0x110
ALU
IF
Reg
Mem
Reg
Early branch resolution at ID stage doesn’t help here coz we still need the value in $1 to decide – which is forwarded from MEM to the ID stage.
bubble
Reg
IF
ALU
Mem
Reg
bubble
bubble
At this cycle, decode stage found the beq instruction. But by then, the following add would have been fetched.
Normal execution resumes at CC7 with a new PC.
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
CC9
CC10
CC11
The two bubble here is due to the RAW dependency between the lw and the beq.

## Slide 40
Reg
# PC = 0x10c
add $3,$2,$1
# PC = 0x108
beq $1, $0, L
# PC = 0x104
lw $1, 0($1)
# PC = 0x100
add $1, $2, $3
ALU
IF
Reg
Mem
Reg
ALU
IF
Reg
Mem
Reg
IF
ALU
Mem
Reg
bubble
Taken!
If taken
# PC = target
ALU
IF
Reg
Mem
Reg
Early branch resolution at ID stage doesn’t help here coz we still need the value in $1 to decide – which is forwarded from MEM to the ID stage.
bubble
IF
bubble
bubble
Target execution starts at CC7 later with a new PC.
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
CC9
CC10
CC11
The add instruction is turned into a NOP.
bubble
bubble
bubble
bubble
There is no cycle difference between taken and not taken as the 2 cycle delay for lw-beq dependency (with the beq being resolved in ID stage) gave enough time for the PC to be changed to the target.
Q4b

## Slide 41: End of Tutorial 10
Slides uploaded on github.com/theodoreleebrant/TA-2425S1
Email: theo@comp.nus.edu.sg
Anonymous feedback:
bit.ly/feedback-theodore
(or scan on the right)
(Also reminder for me to take attendance)