## Slide 1: CS2100 Tutorial 7
Combinatorial Circuits
Slides by Theodore, adapted from Prof. Aaron’s slides

## Slide 2: Announcements (Tutorial 7)
Midterm: results out, please check
  Any queries ask prof Weng Fai / Anandha
Assignment 2: done
  Take your marked paper, Canvas results out on Sunday
Assignment 1: last call
  According to my notes my backlog are done, emails sent
  Last call if I miss anything (Q5, Q1+4+Admin)
Deepavali / Well-being day (in 2 week)
  Mass makeup tutorial (zoom) on Wednesday, auto-attendance
Will start at :05 as usual

## Slide 3: Recap
Adders
Comparators

## Slide 4
Q1.
D3. A combinational circuit takes in a 5-bit input ABCDE and generates a 2-bit value PQ such that PQ represents the distance between the two closest 1s in the input. The distance is defined to be the number of 0s between the two closest 1s.
You may assume that the distance is always determinable from the given input. Therefore, inputs such as 00000 and 01000 will not be supplied to this circuit.
You are to design a circuit to implement a function V(A,B,C,D,E) that takes in input ABCDE and generates output 1 if ABCDE is a valid input for the circuit in question D3 above, or 0 if ABCDE is an invalid input.

## Slide 5
Q1.
Cin
X
Y
Z
Carry
Sum
Full
Adder
Idea?
Cin
Cin
X1
X0
Y1
Y0
2-bit
// adder
Cout
S1
S0
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
Largest subscript: MSB
Smallest subscript: LSB

## Slide 6
Q1.
Cin
X
Y
Z
Carry
Sum
Full
Adder
Cin
Cin
X1
X0
Y1
Y0
2-bit
// adder
Cout
S1
S0
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
Idea?
Count the number of 1’s in ABCDE.
If > 1 then V = 1, else V = 0.
A
B
C
0
E
D
0
0
0
1
0
V
Important: All inputs must be connected to some value! Leave no inputs “hanging”.
Unused outputs may be left alone.

## Slide 7
Q2(a)
A | B | C | D | E | F | G | H
0 | 0 | 0 | 0 |  |  |  | 
0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 0 |  |  |  | 
0 | 0 | 1 | 1 |  |  |  | 
0 | 1 | 0 | 0 |  |  |  | 
0 | 1 | 0 | 1 |  |  |  | 
0 | 1 | 1 | 0 |  |  |  | 
0 | 1 | 1 | 1 |  |  |  | 
1 | 0 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 1 |  |  |  | 
1 | 0 | 1 | 0 |  |  |  | 
1 | 0 | 1 | 1 |  |  |  | 
1 | 1 | 0 | 0 |  |  |  | 
1 | 1 | 0 | 1 |  |  |  | 
1 | 1 | 1 | 0 |  |  |  | 
1 | 1 | 1 | 1 |  |  |  | 
Cin
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
// adder
Cout
S3
S2
S1
S0
EFGH = (ABCD+1)/2
7

## Slide 8
A | B | C | D | E | F | G | H
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
EFGH = (ABCD+1)/2
Cin
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
// adder
Cout
S3
S2
S1
S0
8
Q2(a)

## Slide 9
A | B | C | D | E | F | G | H
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
EFGH = (ABCD+1)/2
Cin
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
// adder
Cout
S3
S2
S1
S0
9
Q2(a)

## Slide 10
P | Q | R | S | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
A1H
Cin
A
B
C
D
E
F
G
H
4221-to-8421 decimal code converter
10
Q2(b)

## Slide 11: Comparison of 8421 and 4221 code
8421 code (BCD)
4 bits for every digit
  Weights for each digits: 8, 4, 2, 1
  e.g. 7 = (8×0)+(4×1)+(2×1)+(1×1) represented as 0111
WXYZ means 8×W + 4×X + 2×Y + 1×Z
4221 code
4 bits for every digit
  Weights for each digits: 4, 2, 2, 1
  e.g. 7 = (4×1)+(2×1)+(2×0)+(1×1) represented as 1101
PQRS means 4×P + 2×Q + 2×R + 1×S

## Slide 12: Converting 4221 to 8421 code
PQRS means 4×P + 2×Q + 2×R + 1×S WXYZ means 8×W + 4×X + 2×Y + 1×Z
S needs to go to Z; as the only representation of 1
We now have
which means that PQ+R = WXY, which is the (second) solution to the A1H (see slide 9 bottom right corner).

## Slide 13
BCD code
13
Q3
Digits: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Code: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001
Given two decimal digits A and B, represented by their BCD codes A3A2A1A0 and B3B2B1B0 respectively, implement a circuit without using any logic gates to calculate the BCD code of the 3-digit output of (51A) + (20(B%2)), where % is the modulo operator. Name the outputs F11F10F9F8 F7F6F5F4 F3F2F1F0.
A |  |  |  | 5A |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  | 
Hint: Fill in the table on the right.

## Slide 14
BCD code
14
Q3
Digits: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Code: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001
A |  |  |  | 5A |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1

## Slide 15
BCD code
15
Q3
Digits: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Code: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111 | 1000 | 1001
A |  |  |  | 5A |  |  |  |  |  |  | 
A3 | A2 | A1 | A0 |  |  |  |  |  |  |  | 
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1

## Slide 16
16
Q3
5A
50A
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1
0
0
0
0
51A

## Slide 17
17
Q3
5A
50A
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1
51A
A3
A2
A1
A0
51A + (20(B%2))

## Slide 18
18
Q3
5A
50A
A3
A2
A1
A0
0
A0
A0
0
0
0
A3
A2
A1
51A
A3
A2
A1
A0
51A + (20(B%2))
B3
B2
B1
B0
B0

## Slide 19
19
Q3
5A
50A
A3
A2
A1
A0
0
A0
A0
0
0
A3
A2
A1
51A
A3
A2
A1
A0
51A + (20(B%2))
B3
B2
B1
B0
B0

## Slide 20
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
F(A,B,C,D) = Sm(12 – 15).
Q4(a)
20

## Slide 21
Q4(b)
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
G(A,B,C,D) = Sm(0, 6, 9, 15).
A | B | C | D | G
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Observe the pattern of ABCD where G=1.
21

## Slide 22
H(A,B,C,D) = Sm(0, 1, 6, 7, 8, 9, 14, 15).
A | B | C | D | H
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
Observe the pattern of ABCD where H=1.
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
Q4(c)
22

## Slide 23
Z(A,B,C,D) = Sm(1, 3, 5, 7, 9, 11, 13).
A | B | C | D | Z
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
Tough!
Cin
X3
X2
X1
X0
Y3
Y2
Y1
Y0
4-bit
COMP
X<Y
X=Y
X>Y
Q4(d)
If this is 1 then it becomes very easy.
23

## Slide 24: End of Tutorial 7
Slides uploaded on github.com/theodoreleebrant/TA-2425S1
Email: theo@comp.nus.edu.sg
Anonymous feedback:
bit.ly/feedback-theodore
(or scan on the right)
(Also reminder for me to take attendance)